## Slide 1: LTspice and SPICE Simulation

## Slide 2: Simulation of Circuits
What is the Voltage at Vb?
SPICE is one of the alternatives to solving the problem by hand.
Notes: (Hint: Vb == 15 V, The Circuit is symmetric about Vb)

## Slide 3: Menus: Left Side of Toolbar
Control Panel
Save (Ctrl+S)
New File (Ctrl+N)
Auto-Fit Graph
Zoom Function(s)
HALT Simulation
RUN Simulation

## Slide 4: Menus: Right Side of Toolbar
Spice Directive (S)
Undo (F9)/Redo (Shift+F9)
Move [Large] Drag [Small]
Generic Component (F2)
Diode (D)
Inductor (L)
Capacitor (C)
Resistor (R)
Command (Hotkey)
Label Net (F4)
Ground (G)
Draw Wire (F3)
Mirror (Ctrl+E)
Rotate (Ctrl+R)

## Slide 5: Components: Common Names
Sources
  Current Source “current”
  Voltage Source “voltage”
Switches
  Switch “sw”
Bipolar Junction Transistors (BJT’s)
  NPN BJT “npn”
  PNP BJT “pnp”
Metal-Oxide Semiconductor Field Effect Transistors (MOSFET’s)
  N-Channel MOSFET “nmos”
  P-Channel MOSFET “pmos”

## Slide 6: Components: Voltage Sources
Interesting Settings Under “Advanced”

## Slide 7: Voltage Sources: Sine Waves
Amplitude is PEAK Voltage
Peak Voltage = 1.414*RMS V
Use {…} to enclose expressions
(Ctrl+Click) Trace Name to show plot Average and RMS

## Slide 8: Voltage Sources: Square Wave
(Trise, Tfall) Very small, DO NOT LEAVE BLANK

## Slide 9: Voltage Sources: Triangular Waves
http://www.analog.com/en/technical-articles/ltspice-generating-triangular-sawtooth-waveforms.html
Start Time [s]
Start Voltage [v]
Peak Time [s]
Peak Voltage [v]
(1 ns After)
Stop Voltage [v]
Start Time [s]
Start Voltage [v]
Peak Time [s]
Peak Voltage [v]
Stop Time [s]
Stop Voltage [v]
Sawtooth Wave
Triangular Wave

## Slide 10: Components: Switches
Spice Directive is REQUIRED
  “.model VALUE SW()”
    Simplest Switch
    “VALUE” is the Value (Name) of the Switch
“SW(…)” Additional Parameters:
  On Resistance: “Ron=“
  Off Resistance: “Roff=“
  Trigger Voltage: “Vt=“
  Hysteresis Voltage: “Vh=“
Component Attribute Editor
  (Right-Click) the Component
http://www.analog.com/en/technical-articles/ltspiceiv-voltage-controlled-switches.html

## Slide 11: Components: Op-Amps
Components > Opamps > UniversalOpamp2
Net Names can be used to connect terminals without wires.
Voltage Sources can be cascaded in series. This particular arrangement is a common for +/- V.

## Slide 12: Components: Transformers
Inductors are coupled using a spice directive
  “K# L# L# Coupling”
  Multiple Inductors can be mutually coupled by listing them before the coupling coefficient.
Coupling ranges from 0 (none) to 1 (complete)
http://www.analog.com/en/technical-articles/using-transformers-in-ltspice-switcher-cadiii.html
Not Great. Do NOT expect power to be conserved.
PRIMARY MUST HAVE SERIES RESISTANCE

## Slide 13: Simulation: AC Analysis
(1) Configure Simulation as “AC Analysis”
(2) Configure Source as (AC)
(3) Simulate

## Slide 14: Simulation: Transient Analysis
(1) Click Here
Simulate the Presented Assuming Sources Were Just Connected
When to Stop [S]: (Keep this small)
  A few periods/few time constants
  Shorter will capture transients
  Longer takes longer to simulate
  (100’s ms) likely sufficient
Time between successive calculations
  Smaller times are more accurate
  Much smaller than resolution
    (1 us) good to 100 kHz
    (100 ns) good to 1 MHz
    (10 ns) good to 10 MHz
    …
Skip initial operating point solution
  Translated: “Don’t guess the steady-state solution before simulating”
  Highly Recommended.

## Slide 15: Simulation: Simple Plotting
A: Click on Wires to add Voltages
B: Click on Components to add Currents (Note the Current Arrow)
Right-Click Axis to Manually Specify Limits
(Defaults to Auto-Fit Everything)
NOTE: Double Clicking Current/Wire Clears all OTHER traces.

## Slide 16: Simulation: Advanced Plotting
(Right-Click) > “Add Traces” or (Right-Click) Existing Trace NAME to open Expression Editor.
Note: (I*V) works better than (I2R)

## Slide 17: Simulation: Known Issues
Discontinuities
  Discontinuous functions and their derivatives tend to break the simulation.
    E.g. Ideal Diodes, Perfect Switches
    “.options gmin=1e-10” [1]
    “.options abstol=1e-10” [1]
    “.options reltol=0.003” [1]
    “.options cshunt=1e-15” [1]
  Magnetic Components
    Shorting voltage sources into inductors
    Transformers
      http://www.ltwiki.org/index.php?title=Transformers
1. http://www.ltwiki.org/index.php?title=Convergence_problems%3F

## Slide 18: Additional Resources
Analog Devices LTspice Download
  http://www.analog.com/en/design-center/design-tools-and-calculators/ltspice-simulator.html
(Unofficial) LTspice Wiki
  http://www.ltwiki.org/index.php?title=Main_Page
Great Walk Though(s)
  http://denethor.wlu.ca/ltspice/#IIIE